|  | Nordisk Sikkerhet AS (NS) |
| --- | --- |
|  | Ref.: Avtale med Statens Strålevern nr. 742, 07/07/2015 |
|  | Project title: “RN Material Detection, Protection, and Dosimetry Equipment for Mukachyvskyi Border Detachment, SBGS” |

Specifications

Supply of Mobile Automated Complex for

the detection of radioactive and nuclear materials

Contracting Authority: Nordisk Sikkerhet AS

Recipient: Mukachyvskiy Border Detachment of SBGS

Tenderer’s name: __________________________________

Contents

1.	TECHNICAL SPECIFICATIONS	1

2.	DOCUMENTATION	3

3.	DELIVERY TERMS AND CONDITIONS	4

4.	TRAINING COURSE: OPERATION, MAINTENANCE AND REPAIR	4

5.	WARRANTY AND POST-WARRANTY SERVICES	5

6.	TIME SCHEDULE	6

NOTE

The Tenderer shall fill in the Annex “Specifications” in the format given below.  The Tenderer’s proposed supplies should be manufactured in accordance with the technical regulations and standards of Ukraine. The complete table should be submitted to the Contracting Authority along with the required tender documents. On the front page of the Annex “Specifications”, the Tenderer shall indicate its name. After the completion of this document, it should be signed and dated by the Tenderer-authorized person.

# TECHNICAL SPECIFICATIONS

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| Manufacturer | — |  |
| Model | — |  |
| Scope of supply | 1 complex |  |
| TECHNICAL SPECIFICATIONS |
| VEHICLE |
| Type | Van |  |
| Number of personnel including driver | ≥5 |  |
| Front seat capacity | Driver + 2 passengers |  |
| Sliding door | 1 |  |
| Rear doors | 2 |  |
| Length, m | ≤ 6 |  |
| Drive | 2x4 |  |
| Gearbox | Manual |  |
| Gears | ≥ 5 |  |
| Motor | Diesel |  |
| Compartment for a car radio (car radio is not included in the scope of this contract) | Yes |  |
| Colour | White |  |
| Climate control system (air conditioner) and heater | Yes |  |
| Service life, no less than | 10 years |  |
| BUILT-IN HARDWARE AND SOFTWARE |
| Built-in radiation/nuclear detection system for automated screening of vehicles (cars, trucks) passing through the detection area | Yes |  |
| Automated workplace of the radiation/nuclear detection system | On the base of industrial type PC having the following or better characteristics: - Intel Core 2 Duo 2,5 GHz; - RAM 2048 MB; - HD 500 GB; - DVD-RW; - Mouse. |  |
| Software for radiation/nuclear detection system and data processing | Yes, installed on PC |  |
| System software for automated workplace | Yes, installed on PC |  |
| Built-in video surveillance, including a built-in infrared illuminator | Yes |  |
| Diesel power generator | Diesel generator shall provide off-line operation within at least 12 hours |  |
| Service life, no less than | 10 years |  |
| LABORATORY COMPARTMENT |
| Wall between the driver’s cabinet and the laboratory | Not required |  |
| Wall between the laboratory and the rear compartment | Yes |  |
| Safety belts at operator’s workplace | ≥ 2 |  |
| Operators’ desk | Yes |  |
| Cupboard and one rack with shelves to store and charge equipment and accessories, including fasteners to fix the instruments on the shelves and shock protection of the equipment | Yes |  |
| Operation from external power supply | AC current, 220 ±10% V, 50±5 Hz |  |
| TECHNICAL COMPARTMENT EQUIPPED WITH RADIATION/NUCLEAR DETECTION SYSTEM |
| Detection channels | Gamma, neutron |  |
| Gamma channel | Plastic scintillator |  |
| Neutron channel | Alternatives to 3He counters are an advantage |  |
| Functions | - Continuous detection of gamma and neutron sources in both modes: (i) during the motion of the mobile complex and (ii) during the stationary mode; - Video surveillance, imaging and recording of alarm-causing objects; - Natural gamma background suppression; - Audible and visual alarm at the operator’s workplace when thresholds are exceeded (different for neutron and gamma alarms); - Adjustable thresholds for alarm. |  |
| Detection zone, no less than | Vertical: 3.0 m Horizontal: 3.0 m |  |
| PERFORMANCE |
| Minimal identified activity of gamma source, no more than: (for the speed of 10 ± 5% km/h, background dose rate ≤ 0.22 µSv/h and the width of detection zone of 3.0 m) |
| 133Ва | 380 kBq |  |
| 137Cs | 420 kBq |  |
| 60Cо | 230 kBq |  |
| Minimal identified neutron flux, no more than (for the speed of 10 ± 5% km/h, background dose rate ≤ 0.22 µSv/h and the width of detection zone of 3.0 m) |
| 252Cf | 1.2(104 neutron/s |  |
| ENVIRONMENTAL REQUIREMENTS |
| Ambient temperatures | From -30 to +45 0C |  |
| Relative humidity | Up to 95% at ambient temperature of 350C and lower, without condensation of moisture |  |
| OTHER REQUIREMENTS |
| Certified for use in Ukraine and/or in other countries | Yes |  |
| Visibility of Norwegian financing | Any equipment delivered under the contract should be clearly identified and should have metallic plates or indelible labels containing the flag of Norway and the phrase “Provided with support from the Government of Norway” in Ukrainian and in English. |  |

# DOCUMENTATION

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| DOCUMENTATION |
| Technical specifications | In English and Ukrainian |  |
| Conceptual design of Mobile Automated Complex | In Ukrainian |  |
| Programme and procedures of factory acceptance test | In English and Ukrainian |  |
| Vehicle documentation | In Ukrainian |  |
| Operator’s manual, including procedure for periodical verification | In Ukrainian |  |
| Passports/logbooks for technical means | In Ukrainian |  |
| Certificate of conformity or equivalent document attesting certification in Ukraine and/or in other countries | In Ukrainian |  |
| Certificate of primary metrological verification for gamma and neutron detectors | In Ukrainian |  |
| Transportation documentation | In English and Ukrainian |  |

# DELIVERY TERMS AND CONDITIONS

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| DELIVERY TERMS AND CONDITIONS |
| Terms of Delivery | DDP, Incoterms 2010 |  |
| Place of Delivery | Mukachevo, Ukraine |  |
| Delivery Time | ≤ 150 calendar days after the date of contract signature |  |

# TRAINING COURSE: OPERATION, MAINTENANCE AND REPAIR

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| TRAINING |
| Training location (to be named by the Recipient) | Mukachyvskyi Border Detachment of SBGS, Ukraine |  |
| Duration of training course | 3 days |  |
| Language of training course | Ukrainian |  |
| Number of trainees, up to | 5 persons |  |
| Themes to be covered | - The nature of gamma and neutron radiation. Radioactive sources and nuclear materials; - The interaction of radiation with matter; - Operating principles of radiation/nuclear detection complex and its units. Gamma / neutron detectors; - Detailed analysis of algorithms and features of operation; - Use of radiation/nuclear detection complex; - Maintenance; - Minor repairs; - Specialized software: installation and operation. |  |
| Theoretical part duration, no less than | 15 hours |  |
| Practical part duration, no less than | 9 hours |  |
| Instructional video | Optional |  |
| Verification | Test, written form |  |
| TRAINING COURSE DOCUMENTATION |
| One certificate per trainee | In Ukrainian and English |  |
| List of materials to provide per trainee | - Set of training materials; - User’s documentation; - Training materials on one CD/DVD. |  |
| Training materials language | In Ukrainian |  |
| Results of test after training should be delivered to the Contracting Authority and Recipient | Yes |  |

# WARRANTY AND POST-WARRANTY SERVICES

|  | Contracting Authority’s Requirements | Tenderer’s Offer |
| --- | --- | --- |
| WARRANTY AND POST-WARRANTY SERVICES |
| Duration of warranty period | ( 24 months |  |
| Place of warranty repairs and maintenance | Ukraine |  |
| Presence of official representative of the manufacturer or authorised service centre in Ukraine | Yes |  |
| Technical support during warranty and post-warranty period | Technical support by email or telephone in Ukrainian/English to solve any technical problems (software failure, anomalous behavior, minor improvements concerning process, functional capabilities of data processing, etc.) and rectify any system-disabled state |  |
| After-sales service | Compulsory after-sales service to be provided under a separate agreement with the Recipient shall include the following: - Maintenance and post warranty repair of the Equipment on the territory of Ukraine; - Rapid provision of spare parts and consumables. |  |

# TIME SCHEDULE

| No. | Action | Period of completion | Tenderer’s Offer |
| --- | --- | --- | --- |
| 1. | Submission of documents: Equipment specifications, Conceptual design. | Within 45 calendar days after the signing of Contract |  |
| 2. | Submission of documents: Programme and procedures of factory acceptance test. | 2 weeks before factory acceptance tests |  |
| 3. | Submission of documents: Operator’s manual, including procedure for periodical verification, Vehicle documents, passports/logbooks for technical means, Certificate of conformity or equivalent document attesting certification in Ukraine and/or in other countries, Transportation documentation. | 2 weeks before the scheduled shipment and supplied with equipment |  |
| 4. | Equipment delivery | Within 150 calendar days after the signing of Contract |  |
| 5. | Training of personnel | Within 150 calendar days after the signing of Contract |  |

Authorized person on behalf of the Tenderer:

Name: ____________________________________________

Title: ______________________________________________

Signature: ________________________________________

Date: ______________________________________________